XYJY-5 Utility Vehicle (Oil Tank) Technical Date

XYJY-5 Utility Vehicle (Oil Tank) Drawing:

| I. Main Technical Date: 主要技术参数： |
| --- |
| 1. | Diesel Engine: 内燃发动机： |  |
|  | Manufacture: 制造厂： | German DUTEZ Company 德国道依茨公司 |
|  | Model: 型号： | F6L912W |
| 2. | Hydraulic Torque Converter and Transmission | 1201FT20000 |
| 3. | Front and Rear Drive Shaft 前后驱动桥 | DANA 112 |
| 4. | Operation Capacity 运行能力 |  |
|  | Climbing Ability: 爬行能力： | 15° |
|  | Driving Speed: 行驶速度： | 1st Gear 0-4.7km/h 2nd Gear 0-10km/h 3rd Gear 0-18.4km/h |
|  | 油罐容积 | 2000L+1000L |
| 5. | Body Swing Axle: 车体摆动角： | ±10° |
| 6. | Steering 转向： |  |
|  | Min. Steering Radius: 最小转弯半径： | Inner: 3750mm 内侧：3750mm | Outer: 5800mm 外侧：5800mm |
| 7. | Weight： 整机重量： | 6900 Kg |
| 8. | Dimensions: 外形尺寸： | 7360mm*1860mm*2000mm(L*W*H) |